## Slide 1: Background
Chiral in nature
Sharma, Vivek, et al. science 325.5939 (2009): 449-451.
Khorasaninejad, M., et al. Nano letters 16.7 (2016): 4595-4600.
Liu, Na, et al. Nature Photonics 3.3 (2009): 157-162.
Circularly polarized light
The design

## Slide 2: Results
One TestSet: input spectrum
freq
Reflectance
Output designed parameters
Feature | Truth/Prediction | Top Length | Bottom Length | Top Spacer | Bottom Spacer | Angle | normalized error
Set 1 | Truth | 1,400.00 | 1,200.00 | 600.00 | 200.00 | 30.00 | 0.43%
 | Prediction | 1,355.92 | 1,171.69 | 597.96 | 209.58 | 4.31 | 
Set 2 | Truth | 1,300.00 | 1,000.00 | 300.00 | 400.00 | 30.00 | 2.44%
 | Prediction | 1,347.19 | 1,076.66 | 408.98 | 232.18 | 14.48 | 
Set 3 | Truth | 1,500.00 | 1,400.00 | 500.00 | 500.00 | 90.00 | 1.99%
 | Prediction | 1,464.53 | 1,281.33 | 503.77 | 521.44 | 144.65 | 
Set 4 | Truth | 1,500.00 | 1,100.00 | 300.00 | 300.00 | 120.00 | 2.06%
 | Prediction | 1,475.32 | 1,102.13 | 312.44 | 341.79 | 63.81 | 
Set 5 | Truth | 1,100.00 | 1,600.00 | 500.00 | 500.00 | 180.00 | 2.34%
 | Prediction | 1,042.84 | 1,531.27 | 479.99 | 467.48 | 120.37 | 
Test set | Truth | 1,500 | 1,400 | 500.00 | 500.00 | 90
 | Prediction | 1,464.53 | 1,281.33 | 503.77 | 521.44 | 144.65
TestLoss
TrainLoss
epoch: 2000
epoch: 2000
0.04
0.1
More test sets:

## Slide 3: Conclusion
We have built up and train a neural network model with the database of chiral meta-materials
We utilize tensor flow to construct the neural network, which is constructed with a 2D convolutional layer, a pooling layer, a fully-connected layer and a output layer
The neural network takes input with the target spectrum with chiral response; and output the designed parameters
The neural network show good performance on parameters l1, l2, t1 and t2, but less good results for rotation angle alpha
It took least than 30mins to train the model with 2000 epochs; this dramatically reduce the time for meta material design, compared with traditional method of parameter sweeping with numerical simulations